## Slide 1: Bluetooth within IoT
Darius Jecu
17026840

## Slide 2: What is IoT?
Embedded devices connected to the internet
Aim – complete given task
  Adjust temperature
  Connect other devices
  More modern devices answer questions
  Execute command though voice

## Slide 3: What is Bluetooth?
Short Range form of communication
Created in 1994 by Ericsson
Used in mobile phones, computers, as well as smart devices
Aim – exchange data + individual data

## Slide 4: Why is Bluetooth needed in IoT?
Embedded devices that connect to the internet to complete specific tasks.
Can’t connect by themselves alone.
Need external device to either send data, or receive input
Bluetooth provides this service.

## Slide 5: How it works in a nutshell
Master and Slave method
  Master device gets info from slave device
  Slaves cannot talk to other slaves
Communicate by broadcasting IP address
  Generic Access Profile (GAP) - “is responsible for managing connections, advertisements, discovery and security features”. (Afaneh, M. 2017).
  Connected devices connect as a Generic Attributes Profile (GATT)
    Exclusive connection

## Slide 6: Connected devices in Bluetooth
Master device can connect to 8 Slave devices at a time
  Piconet
Where connection is made from two or more piconets  scatternet
Sufficient in Bluetooth 5

## Slide 7: Bluetooth 4 – Bluetooth Low Energy (BLE)
Significantly lower consumption
Used for the transfer of small amount of data
Interacts with proximity sensors as well
3 main software levels
  Application, Host and Controller

## Slide 8: Bluetooth 5 – Bluetooth Mesh (BM)
Scatternets allow piconets to communicate  multiple devices communicate with each other
  Lighting as an example
BM connects to device’s destination
  No need for device to be nearby
  Enables both devices to become Master and Slave

## Slide 9: BLE and Bluetooth 5 in depth
BLE devices can send data periodically
  Time, temperature, heart rate
  Distance rage of 30-100 meters
Bluetooth 5 designed bearing in mind IoT
  Low energy
  Low value
  Double speed of 2mb/s ≠ BLE has 1mb/s
  Increased packed size over a wider range & higher speed

## Slide 10: Security of Bluetooth
Fairly secure
  Requires device to be nearby + requires device to accept communication with each other
3 stages of security
  Authentication, Confidentiality, Authorisation
4 security modes
  Increasing security from mode 1 to mode 4
The older the device, the less secure

## Slide 11: Security concerns of Bluetooth
If not secure connection, could be rather easily hacked
3 main shapes of hacking
  Bluejacking
    Misleading recipient
  Bluebugging
    Taking over functions of device
  Car whispering
    Hackers send and receive audio to and from car system

## Slide 12: Potential competitors of Bluetooth – Wi-Fi
Wi-Fi pros:
Throughput is higher
Low cost infrastructure
More easily deployed
Configured in more devices as standard.
Bluetooth pros:
Less amount of energy required
Cheaper to use
Allows network to expand if device is nearby

## Slide 13: Potential competitors of Bluetooth - LoRa
LoRa pros:
Range of up to 10 miles between devices
10 years battery life
Improves robustness to interference, noise & jamming
High accuracy localisation and ranging
Sensors can be spread across wide large area
Licence free
HOWEVER
Still not as cheap implementation as Bluetooth
Non-implementation of LoRa in devices nowadays  less appealing to developers

## Slide 14: Conclusion
Bluetooth became increasingly developed within IoT
Bluetooth Mesh pushed the boundaries in IoT market.
Challenged Wi-Fi as top communication method.
Security is quite strong.
Thank you!